## Slide 1
AI-POWERED ELEVATOR DISPATCH
Two Problems.
One Smart System.
How Computer Vision & AI can solve the Missed Batch problem
and the Dangerous Door-Close problem in large buildings.
Problem 1 — The Missed Batch
Problem 2 — The Dangerous Close

## Slide 2
PROBLEM 1
The Missed Batch Scenario
FL 30
FL 2
FL 1
🛗
👥
01
Elevator reaches Floor 2
Passengers board. Doors close. Elevator commits to heading up toward Floor 30.
02
New batch arrives at Floor 1
A large group arrives at Floor 1 just after doors close and presses the call button.
03
Elevator ignores Floor 1
Floor 1 was not pre-registered. Elevator skips it — even with empty cabin space.
04
Full 30-floor round trip to wait
Group waits for the elevator to travel 28 floors up, serve riders, then return. Minimum 5–10 minutes wasted in high-rise buildings.

## Slide 3
PROBLEM 2
The Dangerous Door-Close
Context: In large high-rise buildings (30F+), odd and even floors often use separate elevator banks. Riders must choose correctly — then race to make it before doors close.
01
Rider identifies correct elevator bank
In a 30F+ building, odd-floor riders use one bank, even-floor another. This split adds confusion, walking time, and forces quick decisions under pressure.
02
Doors start closing
An existing rider inside presses the close button — intentionally or impatiently — before everyone has boarded.
03
Latecomers run for the door
A rider seeing the doors closing runs toward the elevator. This creates a collision risk and potential injury at the door threshold.
04
Rider is missed — must wait again
Even if they avoid injury, they miss the elevator entirely and must wait a full cycle — especially painful in high-traffic peak hours.

## Slide 4
THE SOLUTION
One AI Vision System — Two Fixes
Shared Core: Multi-camera input (lobby + cabin) → Computer Vision person detection + occupancy tracking → AI dispatch controller
Fix 1 — Dynamic En-Route Stop
📷 Cabin camera
CV model counts passengers inside, computes % occupancy continuously
📡 Floor call signal
AI scans neighbouring floors (above & below current route) for pending calls
⚖️ Cost evaluation
If cabin has capacity AND neighbouring floor is within detour threshold → insert stop; otherwise skip
✅ Result
Waiting group boards mid-journey. If the current bank is >80% utilised, the controller polls the adjacent odd/even bank and redirects the call if floor parity allows and spare capacity exists.
Fix 2 — Approaching Rider Hold
📷 Lobby camera + CV
Wide-angle camera tracks corridor; CV model classifies each person as 'boarding' or 'passing' based on gait speed, direction & trajectory
🚫 Door hold
If a 'boarding' rider is detected, close-button signal is suppressed for a grace window (e.g. 4 sec) — then doors close normally
🔐 Rider memory
Optional face/gait ID for registered occupants (opt-in). Default: anonymised motion-only — no identity stored
✅ Result
Approaching rider boards safely — no running, no collision risk. Privacy trade-offs addressed in detail on next slide.

## Slide 5
FIX 2 — DEEP DIVE
How Rider Memory & Hold Logic Works
📷
Lobby Cam
Tracking
Wide-angle camera monitors the lobby corridor. CV model tracks all individuals — direction, speed, and movement trajectory.
▶
🏃
Approach
Classifier
CV model predicts boarding intent from gait speed, direction & path — classifies 'likely boarding' vs 'passing through'. No face ID required.
▶
🧠
Rider
Memory
Optional: face/gait recognition for registered occupants. Privacy concern — face recognition requires explicit opt-in consent; motion-only is the default fallback.
▶
🚫
Close Button
Override
If an approaching rider is detected, the close-button signal is suppressed. Doors remain open for a grace window (e.g. 4 sec).
▶
✅
Safe
Boarding
Rider boards safely. No running, no collision risk. Once boarded (or timer expires), doors close normally.
⚠ Privacy: Camera-based prediction inherently raises surveillance concerns. Mitigations: no face data stored, opt-in only, motion vectors anonymised, GDPR/local law compliant by design.

## Slide 6
IMPLEMENTATION & IMPACT
What's Needed & What We Gain
Tech Components
📷 Cabin Camera
CV headcount + occupancy tracking; runs on edge node inside cabin
📷 Lobby Camera
Wide-angle; tracks individuals, predicts boarding intent via speed & trajectory
🧠 CV + Gait Model
Classifies boarding intent; opt-in face recognition; anonymised motion fallback
📡 Floor Call API
Soft integration with existing call-button controller
⚙️ AI Dispatch Controller
Manages dynamic stops, door hold overrides & odd/even bank re-routing when one bank is overloaded
Problem 1 — Missed Batch
↓ 60%
Unnecessary full-trip waits (est.)
↑ 40%
Cabin utilization (est.)
Problem 2 — Dangerous Close
↓ 90%
Door-close incidents (est.)
↓ 35% missed-boarding events (est.) · Works on existing hardware · Minimal retrofit · All figures estimated